## Slide 1: Hardware Descriptive Language (HDL)
Lecture # 2
1

## Slide 2: Motivation for HDL
2
Classical Design relied on
  Schematics & Manual methods
But today
  Computer Based Languages (HDL)
    Because of the design circuits size & complexity
Language based designs
  Independent of technology
  Avoids the laborious steps involved in manual design

## Slide 3: Cont’d…
3
HDL & Synthesis tool focus engr’s attention on
  Functionality rather than gates
Synthesized ckt realize the desired functionality, area, performance constraints
Alternative architecture can be generated from the same HDL model & evaluated quickly to perform design tradeoffs.

## Slide 4: Building binary digital solutions to computational problems

## Slide 5
Logic synthesis using a Hardware Description Language (HDL) automates the most tedious and error-prone aspects of design

## Slide 6: Why do we need HDLs ?
6
HDL can describe both circuit structure and behavior
  Schematics describe only circuit structure
  C language describes only behaviors
Provide high level abstraction to speed up design
High portability and readability
Enable rapid prototyping
Support different hardware styles

## Slide 7: What do we need from HDLs ?
7
Describe
  Combinational logic
  Level sensitive storage devices
  Edge-triggered storage devices
Support for hardware concurrency

## Slide 8: HDLs
8
Verilog
  Language style close to C/C++
  Pre-defined data type, easy to use
VHDL
  Language style close to Ada
  User-defined data type, more flexible
Equally effective, personal preference
Both are supported by synthesis tool for ASIC & FPGAs
Both are IEEE Standards
Verilog has 60% of the world digital design market (larger share in US)

## Slide 9: Verilog HDL

## Slide 10
Verilog HDL Basics
  Verilog was introduced in 1984 by Gateway Design System Corporation, now a part of Cadence Design Systems
  Verilog-based synthesis tool introduced by Synopsys in 1987
  Verilog HDL is a Hardware Description Language.
  It describes the hardware. It is not a programming & procedural language.
  Verilog HDL is a concurrent language
  It enables specification of a digital system at a range of levels of abstraction:
    Switches, Gates, RTL, and higher
  Standard: IEEE 1364 in 1995

## Slide 11: Event Driven Simulation
Verilog is really a language for modeling event driven systems
– Event : change in state
Simulation starts at t = 0
Processing events generates new events
When all events at time t have been processed simulation time advances to t+1
Simulation stops when there are no more events in the queue

## Slide 12
Basic Limitation of Verilog
Description of digital systems only

## Slide 13: Abstraction Levels in Verilog

## Slide 14
Switch-Level Modeling
This is the lowest level of abstraction provided by Verilog. A module can be implemented in terms of switches and the interconnections between them. Design at this level requires knowledge of switch-level implementation details (It’s rarely used). It is feasible for small circuits.
Gate Level Modeling
The module is implemented in terms of logic gates and interconnections between these gates. Design at this level is similar to describing a design in terms of a gate-level logic diagram. It is feasible for small circuits. Verilog supports basic logic gates as predefined primitives.
Dataflow Modeling
At this level, the module is designed by specifying the data flow. The designer is aware of how data flows between hardware registers and how the data is processed in the design.
Behavioral Modeling
This is the highest level of abstraction provided by Verilog HDL. A module can be implemented in terms of the desired design algorithm without concern for the hardware implementation details. Designing at this level is very similar to C programming.