## Slide 1: Hardware Descriptive Language(HDL)
Lecture # 3

## Slide 2: Taste of Verilog
Verilog keywords
Module name Module ports
module Add_half ( sum, c_out, a, b );
input a, b;
output
wire
sum, c_out; c_out_bar;
xor (sum, a, b);
nand (c_out_bar, a, b);
not (c_out, c_out_bar);
endmodule
Declaration of port modes
Declaration of internal signal
Instantiation of primitive gates
c_out
a b
sum
c_out_bar

## Slide 3: Modules
The Module Concept
  Basic design unit
  Modules are:
    Declared
    Instantiated
  Modules declarations cannot be nested
  Everything you write in Verilog must be inside a module exception: compiler directives

## Slide 4: Verilog Module
Description of internal structure/function
  Implementation is hidden to outside world
Communicate with outside through ports
  Port list is optional
module Add_half ( sum, c_out, a, b );
input a, b;
output sum, c_out;
wire c_out_bar;
xor (sum, a, b);
nand (c_out_bar, a, b);
not (c_out, c_out_bar);
endmodule
a b
sum
c_out_bar
c_out

## Slide 5: Components of a Verilog Module

## Slide 6
Identifiers - must not be keywords!
Formed from {[A-Z], [a-z], [0-9], _, $}, but can’t begin with $ or [0-9]
Case sensitivity
  myid ≠ Myid
Ports
Ports are like pins on chip
Type: defined by keywords
  input
  output
  inout (bi-directional)

## Slide 9: Port Connection Rules

## Slide 10
Width matching
It is legal to connect internal and external items of different sizes when making inter-module port connections. However, a warning is typically issued that the widths do not match.
Unconnected ports
Verilog allows ports to remain unconnected. For example, certain output ports might be simply for debugging, and you might not be interested in connecting them to the external signals.
fulladd fa0(SUM, , A, B, C_IN); //Output port c_out is unconnected

## Slide 11: Connecting Ports to External Signals
Connecting by ordered list
  The signals to be connected must appear in the module instantiation in the same order as the ports in the port list in the module definition.
Connecting ports by name
  You can specify the port connections in any order as long as the port name in the module definition correctly matches the external signal.

## Slide 12: Ports Connections
By order
By name
Empty port
module child( a, b, c );
…
Endmodule
/////////////////////////////////////////////////
module parent;
wire u, v, w;
child m1( u, v, w );
child m2( .c(w), .a(u), .b(v) ); child m3( u, , w );
endmodule

## Slide 13
Comments
// The rest of the line is a comment
/* Multiple line comment */
/* Nesting /* comments */ do NOT work */

## Slide 14: Verilog Primitives
Basic element to build a module, such as
nand, and, nor, buf and not gates
Never used stand-alone in design, must be within a module
Pre-defined or user-defined
Identifier (instance name) is optional
Output is at left-most in port list
Default delay = 0

## Slide 15: Primitives
Gate Level
  and, nand
  or, nor
  xor, xnor
  buf , not
  bufif0, bufif1, notif0, notif1 (three-state)
Switch Level

## Slide 16: Smart Primitives
module nand3 ( O, A1, A2, A3 );
input output
A1, A2, A3; O;
nand ( O, A1, A2, A3 );
endmodule
Same primitive can be used to describe for any number of inputs
This works for only pre-defined primitives, not UDP

## Slide 18: Simulation Component
Unit Under Test
Unit Under Test
Stimulus generator
Design Unit Test Bench
Response monitor

## Slide 19: Structured Design Methodology
Design: top-down
Verification: bottom-up

## Slide 20: Hierarchical Description
a
b
c_in
M1
Add_half
M2
Add_half
sum
c_out
Nested module instantiation to arbitrary depth
xor
nand
not
Add_half
xor
nand
not
Add_half
or
Add_full
M1
M2

## Slide 21: Two main data types
Nets
Net represent connections between hardware elements.
  Just as in real circuits, nets have values continuously driven on them by the outputs of devices that they are connected to.
Do not hold their values
Can be thought as hardware wires driven by logic
Cannot be assigned in initial & always block
Equal z when unconnected
Undeclared Nets - Default type
  Not explicitly declared default to wire

## Slide 22: Reg
Registers represent data storage elements.
Registers retain value until another value is placed onto them.
– Do not confuse the term registers in Verilog with hardware registers built from edge-triggered flip flops in real circuits.
Variables that store values
Do not represent real hardware but real hardware can be implemented with registers

## Slide 23: Example 2x1 MUX
module mux_2to1(a,b,sel,f);
output f;
input a,b,sel;
and g1(f1,a,nsel);
and g2(f2,b,sel);
or g3(f,f1,f2);
not g4(nsel,sel);
endmodule

## Slide 24
module stimN();
reg A,B,SEL;
wire F;
mux_2to1 M(A,B,SEL,F);
initial
begin
$display("A B SEL F");
A=0;
B=0;
SEL=0;
#1 $display("%b %b %b %b",A,B,SEL,F);
#5 A=0;
B=0;
SEL=1;
$display("%b %b %b %b",A,B,SEL,F);
#10 A=0;
B=1;
SEL=0;
$display("%b %b %b %b",A,B,SEL,F);
#15 A=0;
B=1;
SEL=1;
$display("%b %b %b %b",A,B,SEL,F);
#20 A=1;
B=0;
SEL=0;
$display("%b %b %b %b",A,B,SEL,F);
# 25 A=1;
B=0;
SEL=1;
$display("%b %b %b %b",A,B,SEL,F);
#30 A=1;
B=1;
SEL=0;
#35 $display("%b %b %b %b",A,B,SEL,F);
A=1;
B=1;
SEL=1;
$display("%b %b %b %b",A,B,SEL,F);
end
endmodule