## Slide 1: Hardware Descriptive Language(HDL) Gate level Modeling Data flow Level Modeling
Lecture # 4

## Slide 2: Taste of Verilog
Verilog keywords
Module name Module ports
module Add_half ( sum, c_out, a, b );
input a, b;
output
wire
sum, c_out; c_out_bar;
xor (sum, a, b);
nand (c_out_bar, a, b);
not (c_out, c_out_bar);
endmodule
Declaration of port modes
Declaration of internal signal
Instantiation of primitive gates
c_out
a b
sum
c_out_bar

## Slide 3: Gate Level Verilog code Decoder 3x8
module task1(a,b,c,d0,d1,d2,d3,d4,d5,d6,d7);
input a,b,c;
output d0,d1,d2,d3,d4,d5,d6,d7;
not g10(na,a);
not g11(nb,b);
not g12(nc,c);
and g0(d0,na,nb,nc);
and g1(d1,na,nb,c);
and g2(d2,na,b,nc);
and g3(d3,na,b,c);
and g4(d4,a,nb,nc);
and g5(d5,a,nb,c);
and g6(d6,a,b,nc);
and g7(d7,a,b,c);
endmodule

## Slide 4: Gate Level Verilog code Decoder 3x8
module stim_task1();
reg A,B,C;
wire D0,D1,D2,D3,D4,D5,D6,D7;
task1 inst(A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);
initial
begin
$display("A B C D0 D1 D2 D3 D4 D5 D6 D7");
A=0;B=0;C=0;
#1 $display("%b %b %b %b %b %b %b %b %b %b %b",A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);
A=0;B=0;C=1;
#1 $display("%b %b %b %b %b %b %b %b %b %b %b",A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);
A=0;B=1;C=0;
#1 $display("%b %b %b %b %b %b %b %b %b %b %b",A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);

## Slide 5
A=0;B=1;C=1;
#1 $display("%b %b %b %b %b %b %b %b %b %b %b",A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);
A=1;B=0;C=0;
#1 $display("%b %b %b %b %b %b %b %b %b %b %b",A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);
A=1;B=0;C=1;
#1 $display("%b %b %b %b %b %b %b %b %b %b %b",A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);
A=1;B=1;C=0;
#1 $display("%b %b %b %b %b %b %b %b %b %b %b",A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);
A=1;B=1;C=1;
#1 $display("%b %b %b %b %b %b %b %b %b %b %b",A,B,C,D0,D1,D2,D3,D4,D5,D6,D7);
end
endmodule

## Slide 6: Dataflow Level Modeling
Dataflow modeling provides the means of describing combinational circuits by their function rather than by their gate structure.
This approach allows the designer to focus on optimizing the circuit in terms of the flow of data.
Dataflow modeling uses several operators that act on operands to produce the desired results

## Slide 7: Dataflow Verilog code Decoder 2x4
module dec_2_to_4(input [1:0]in,output [3:0]out);
assign out[0] = (~in[1] & ~in[0]);
assign out[1] = (~in[1] & in[0]);
assign out[2] = (in[1] & ~in[0]);
assign out[3] = (in[1] & in[0]);
endmodule
Assign keyword

## Slide 8: Dataflow Verilog code Decoder 2x4
module stim_task1();
reg [1:0]IN;
wire [3:0]OUT;
dec_2_4 dec(IN,OUT);
initial
begin
#1 $display("In |Out");
#2 IN[1]=0;IN[0]=0;
#1 $monitor("%b |%b",IN,OUT);
#3 IN[1]=0;IN[0]=1;
#4 IN[1]=1;IN[0]=0;
#5 IN[1]=1;IN[0]=1;
end
endmodule

## Slide 9: Home Task Lab 1
Write a Verilog code for 2x4, 3x8 and 4x16 decoder using Gate Level modeling.
Write a Verilog code for 2x1, 4x1 and 8x1 multiplexer using Gate Level modeling.

## Slide 10: Home Task Lab 2
Write a Verilog code for Half Adder using Gate Level modeling.
Write a Verilog code for Full Adder using Gate Level modeling.
Write a Verilog code for Half Subtractor using Gate Level modeling.
Write a Verilog code for Adder and Subtractor using Gate Level modeling.

## Slide 11: Home Task Lab 3
Write a Verilog code for 2x4 Decoder using Dataflow Level modeling.
Write a Verilog code for 2x1 MUX using Dataflow Level modeling.
Write a Verilog code for Half Adder using Dataflow Level modeling.
Write a Verilog code for Full Adder using Dataflow Level modeling.
Write a Verilog code for Half Subtractor using Dataflow Level modeling.
Write a Verilog code for Adder and Subtractor using Dataflow Level modeling.